The Abstract Domain of Parallelotopes
Octagon
Box
Parallelotope

---
What is a parallelotope?
A many-dimensional generalization of a parallelogram.
1-dimensional ptope
(interval)
2-dimensional ptope
(parallelogram)
3-dimensional ptope
(parallelepiped)

---
What is a parallelotope?
- Several formal definitions:
  - The sum of linearly-independent segments
    - Hence, a parallelotope is a zonotope
  - The image of a box trough a linear transformation
stack { x' = x+2y+1 # y' = y }

---
Representation of parallelotopes
- A triple <A,m,M>
  - A is an invertible matrix in
  - m, M are vectors in
setR^n
setR^n
stack { - infinity <= x+y <= 1 # -1 <= x-y <= 1 }
{~~~~~~~~~~~~~~~~~~~~~~~} underbrace {A=left ( matrix{ 1 # {phantom 0} 1 ## 1 # -1} right) ~ bold m = left( matrix { -infinity ## -1 } right) ~ bold M = left( matrix { 1 ## 1 } right)}

---
Least parallelotope ?
In this case the least parallelotope exists

---
Minimal parallelotopes
- No least parallelotope, but many minimal ones.
- No Galois connection framework.

---
Relatively optimal parallelotope
- The green square is not minimal
- …. however, its the least correct one of the given shape!
- We call it relatively optimal

---
Semantic Transformers
- Concrete transformers
  - Assignment
    - Invertible, Non-deterministic, Non-invertible
  - Refinement by linear inequality
  - Union
- We strive to find abstract transformers which are
  - g-complete
  - Minimal
  - Relatively optimal

---
Inv. Assignment: x'=x+2y+1
Invertible affine transformations map parallelotopes to parallelotopes.
x' = x + 2y +1
alignl stack{ 0 <= x'-2y+1 <= 2 # 0 <= y <= 1 }
stack{ 0 <= x <= 1# 0 <= y <= 1}
g-complete!

---
Non-deterministic Assignment
Sum of the parallelotope with a line
P+l
l
P

---
Non-det. Assignment: x=?
If P lies in a hyperplane p' which is not orthogonal to p, then p(P) is a parallelotope.

---
Non-det. Assignment: x=? (good case)
stack { 3 <= x+y+z <= 3 # 0 <= y-z <= 1 # 0 <= -2x + y + z <= 1 }
x appears in an
equation
Normalize, replacing x with 3-y-z in all the other inequations
stack { 3 <= x+y+z <= 3 # 0 <= y-z <= 1 # 6 <= 3y + 3z <= 7 }
Remove bounds in the equation
stack { - infinity <= x+y+z <= + infinity # 0 <= y-z <= 1 # 6 <= - y - z <= 7 }
g-complete!

---
Non-det. Assignment: x=? (bad case)
x appears only in
inequations
stack { 0 <= x+y+z <= 3 # 0 <= y-z <= 1 # 0 <= -2x + y + z <= 1 }
Combine first inequation where x appears with all the others to remove x.
stack { 0 <= x+y+z <= 3 # 0 <= y-z <= 1 # 0 <= 3y + 3z <= 7 }
Remove bounds in the equation
stack { - infinity <= x+y+z <= + infinity # 0 <= y-z <= 1 # 6 <= - y - z <= 7 }
minimal

---
Non-invertible Assignment: x=2y+z-1
stack { - infinity <= x+y+z <= + infinity # 0 <= y-z <= 1 # 6 <= - y - z <= 7 }
stack { -1 <= x - 2y -z <= -1 # 0 <= y-z <= 1 # 6 <= -y-z <= 7 }
stack { 0 <= x+y+z <= 3 # 0 <= y-z <= 1 # 0 <= -2x + y + z <= 1 }
non-det.
assignment
replace the only row
containing x
with the new equation
minimal or g-complete

---
Linear refinement: -2x+y ≥ 0
Easy case:
choose an ubounded
line
stack { - infinity <= x+y <= + infinity # -1 <= x-y <= 1 }
stack { 0 <= -2x + y <= + infinity # -1 <= x-y <= 1 }
linear
independent
g-complete!

---
Linear refinement
keep the same shape
replace a bound
relatively optimal

---
Union (weak)
The weak union is similar to join of template polyhedra.
chose on shape
or the other

---
Union (weak)
Weak union never creates new constraints
we want
weak union

---
Union (inverse join)
- A smarter union based on inverse join
  - collect all the linear forms of the bounding hyperplanes
    - for the original parallelotopes
    - generated by inversion
  - prioritize them according to some heuristics
  - choose a subset of linear forms which is linearly independent and maximize priorities
  - compute the relatively optimal parallelotope with the shape given by the choosen linear forms

---
Collecting linear forms
linear form generated
by inversion
linear forms in the
original ptopes

---
Prioritizing linear forms
For each linear form, compute the bounds for the original parallelotopes
Bounds are the same
Priority 1

---
Prioritizing linear forms
For each linear form, compute the bounds for the original parallelotopes
Bounds intersect
Priority 2

---
Prioritizing linear forms
For each linear form, compute the bounds for the original parallelotopes
Bounds do not intersect
Priority 3

---
Choose linear forms
- Collect
  - In order of priority
  - Until we get a linearly independent set
- Easy in this case
- In the general case, follow
  - Gaussian elimination
  - or QR factorization

---
Precision
- Parallelotope is
  - More precise than Karr's analysis
  - Less precise than polyhedra
    - with standard join or inverse join
  - Incomparable with all the other domains
    - even with interval domain

---
Complexity
Operation	Parallelotopes	Karr's lin. eq.	Octagons
Inv. Assignment	n2	n2	n2
n.d. Assignment	n2	n2	n
n.I. Assignment	n2	n2	n2
Refinement	n3		n3
Union	n4		n3
Widening	n3	--	n3

---
Example
- Invariants
  - 3i – j + k = 1
  - 2 ≤ i
  - k+5 ≤ j
i = 2
j = k+5
While (TRUE) {
  i = i+1
  j = j+3
}
Found by parallelotope
analysis
implied by the first twos

---
Example
- Invariants:
  - i+2j ≤ 6
  - 0 ≤ j
  - 2j – i ≤ -2
i = 2
j = 0
while (TRUE) {
if (i*i==4)
i = i+4
 else {
j = j+1
i = i+2
}
}
Found by parallelotope
analysis
found during inversion join,
but discharged in favor of
the first twos

---
Strong and weak points
- Strong points
  - No limits on the complexity of constraints
  - Reasonably fast
- Weak points
  - Very few constraints may be handled simultaneously
  - Require rational arithmetic when analyzing floating point variables

---
How to improve
- Parallelotope as an auxiliary domain
  - To be combined with domains such as Octagon, TVPI, Interval
  - The base domain compute the “standard invariants”
  - For constraints outside the reach of the standard domain, parallelotopes may help
- How to combine?
  - Reduced product? Difficult
  - Transfer function between the two domains
  - Need to tune Parallelotope to avoid invariants handled by the base domain